## Slide 1: Welcome at this IEC 61131-3 Tutorial
Notes: Welcom in the notes view,
showing you the notes / additional text for this presentation
Success!

## Slide 2: Harmonizing the way people look to control
the future is here
Eelco van der Wal
Managing Director PLCopen
Notes: This presentation is not about standards
It is about the way people look to control

## Slide 3: Fiction?
Imagine
* you are in industrial control
* working with 4 different brands of controls
* using different dialects in their programming languages
* strugling to match the level of your software engineers with the electrical engineers / maintenance on the factory floor
* & seeing that your competitor does better
Why? What’s wrong ?
Notes: If the situation above looks like your reality………………

## Slide 4: Out of the jungle
The current variety of problems can be vastly reduced via standardization
... and such a standard is available
Notes: …….. you’d better harmonize the way you all look to control

## Slide 5
IEC 61131-3
“The best thing that happened to industrial control”
Sugar Lantic on Automation Maillist
Notes: … via the IEC 1131-3 standard
First, let us take a closer look into IEC 1131-3.
This is the english version (waving with the standard itself). It contains
a lot of information, so it is better if we focus to the benefits for you.

## Slide 6: The 7 parts of the IEC 61131 Standard
- 1 General overview, definitions
- 2 Hardware
- 3 Programming Languages
- 4 User Guidelines
- 5 Messaging Service Specification
- 7 Fuzzy Logic
- 8 Implementation guidelines
Notes: As you can see it consists of five parts.
Part 1 till 3 are International Standards
Part 1 provides the general overview
Part 2 defines the requirements and test procedures for the hardware.
These include elelctrical, mechanical and functional requirements
service, storage and transportation conditions
and test methods and procedures for verification of compliancy
Part 3 deals with Programming Languages.
These programming languages not only suit Programmable Controllers, but effectively every environment within industrial control and automation.
There are many ways to look at this standard…...

## Slide 7: IEC 61131-3 Programming languages / Industrial Control Programming
The interface between the programmer and the control system
Notes: … but just to make sure we are all talking about the same:
the programming languages deals with the interface between
the programmer and the control system
or more direct: what this man sees on his screen

## Slide 8: IEC 61131-3 Programming languages / Industrial Control Programming
...with support for people
with different backgrounds
Notes: or, within IEC 1131-3, how these people interface to ther control,
no matter which background / color, or level
current environments incorporate them all
Meaning: support for teams with people of different level
or background

## Slide 9: What is the Benefit of such a Standard ?
Notes: see above

## Slide 10: Users? Which Users?
Education
Installation
Maintenance
Programming
Process cntrl
Discrete Mnf
System Integrator
YOU ??
Notes: Thefirst problem is: which users?
Where are you, or your company, in this picture?

## Slide 11: Users? Which Users?
Automobile production lines
Water treatment plant
Food processing and packaging machinery
Cable manufacturing
Semi-conductor clean room automation
Theme-park roller coasters
Nuclear waste treatment plant
This wide range encompass different skills
Notes: IEC 1131-3 is used in such a tremendous broad area, that we only can make some general statements about the advantages

## Slide 12: What is the Benefit of such a Standard
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Notes: see above
One has to learn it only once, and can use it on all systems

## Slide 13: What is the Benefit of such a Standard
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability
(reduced application investment and supplier dependency)
Notes: see above
That creates a focus to the real problem solving part

## Slide 14: What is the Benefit of such a Standard
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Notes: because the dialects are gone and the structuring tools are
available, it lead to a better understanding between the
people involved, and to less errors

## Slide 15: What is the Benefit of such a Standard
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments
(general industrial control)
Notes: IEC 1131-3 is used, and can be used, in a very broad area:
industrial control in general

## Slide 16: What is the Benefit of such a Standard
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments (general industrial control)
Combining harmonously different components from different
locations, companies or countries, or projects
Notes: and is not restricited to one location or project: for instance
function blocks can be reused over an over again

## Slide 17: What is the Benefit of such a Standard
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments (general industrial control)
Combining harmonously different components from different locations, companies or countries, or projects
Increased connectivity (investment protection)
Notes: taking care that your investment is not lost: you are
open to the future

## Slide 18: What is the Benefit of such a Standard
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments (general industrial control)
Combining harmonously different components from different locations, companies or countries, or projects
Increased connectivity (investment protection)
Notes: <<no text initially>>
…. . But there was this other buzzword .. PLCopen

## Slide 19: Key quality features of IEC 61131-3
Structured software - through use of Configuration, Resource and Program Organization Units (POUs)
Strong Data Typing - through languages that restrict operations to only apply to appropriate types of data
Execution control - through use of tasks
Complex sequential behaviour - through Sequential Function Charts
Software encapsulation - through use of POUs, structures and complex data types.
Notes: In general, one can reconcile the following strong points
of IEC 1131-3
see slide

## Slide 20: An example
Fermentation Control System
courtesy of Omron Electronics
Notes: But how does this help you in practice.
Let us look at another example, in this case a fermentation process

## Slide 21: Fermentation Process
Heater band
Acidic reagent
Alkali reagent
Harvest valve
pH sensor
Temperature
sensor
Feed valve
Agitator
Notes: The whole process is drawn here.
There is a large vessel, which vcan be filled (Feed Valve)
with the liquid, can be heated with the heater band (cooling
via convection), which can be stirred via the motor,
and where acid and alcalic fluid can be added into.

## Slide 22: Fermentation control decomposition
MainSequence e.g. top level process steps - filling, heating, agitating, fermenting, harvesting, cleaning.
Valve control e.g. operating valves used to fill and empty the fermentation vessel
Temperature control for monitoring the temperature of the vessel and modulating the heater.
Agitator control for the agitator motor activated as demanded by the main process sequence.
pH Control for monitoring the acidity of the fermentation contents and adding acidic or alkali reagents.
Notes: Overall, one can decompose the process into the
following sections
(see slide)

## Slide 23: Fermentation control program
Notes: If we would present those in the programming language
Function Block Diagram, it could look like this
In this case all basic blocks have been defined, which is one
of the basic steps needed to convert the problem to a solution
(read from left to right side)
(On the left the inputs, on the right the outputs)

## Slide 24: Main sequence SFC
Shows the main
process states
Notes: For the main sequence we would use the structuring tool
Sequential Function Chart.
We start at the top with the Initialization: since we do not know
the status of the system when we first switch it on, we got
to check here the position of the valves, etc.
Then we start filling till the right level has been reached.
Next phase is the heating till the fermentation process starts
If it starts, we get to the next phase: the actual fermentation
process control part
After completion, we harvest, and after that clean, and we are ready
to restart at the top.
This decomposition gives everybody involved a clear overview
which sequences are involved, and how it is further decomposed
into the function blocks which can be programmed in any of
the four languages.
Or, stated differently: our user requirement specification is
(nearly) done!

## Slide 25: IEC 61131-3 Overview

## Slide 26: The IEC 61131-3 Standard
Common Elements
Programming Languages
Notes: There are a lot of ways to look to this part 3 of IEC 1131.
The one we use here is very simple: the standard consists of two main blocks:
the Common Elements, valid throughout the specification
and the Programming Languages
Let us take a closer look to the common elements…….

## Slide 27: The IEC 61131-3 Standard
Common Elements
Programming Languages
Notes: So much about the common elements. Now to the next group:
the programming languages

## Slide 28: The IEC 61131-3 Programming Languages
Instruction List Structured Text
Function Block Diagram Ladder Diagram
C:= A AND NOT B
A B C
-| |--|/|----------------( )
LD A
ANDN B
ST C
AND
A C
B
Notes: 15
Regarding the five standardised programming languages no one should be too worried, because all languages except Structured Text have been widely known and utilised for years.
Different regions of the industrial world as well as different fields of applications have contributed to the selection of those languages.

## Slide 29: The IEC 61131-3 Standard
Common Elements
Programming Languages
Notes: There are a lot of ways to look to this part 3 of IEC 1131.
The one we use here is very simple: the standard consists of two main blocks:
the Common Elements, valid throughout the specification
and the Programming Languages
Let us take a closer look to the common elements…….

## Slide 30: Common Elements include :
Variables, Data Types and Declaration
Configuration, Resources and Tasks
Function, Function Blocks and Programs
Sequential Function Charts

## Slide 31: IEC 61131-3 : Common Elements
Variables
Symbolic representation via labels
Restricted area for I/O mapping
Hardware independent code
What is this?
01010101 10101010
Notes: The first to mention are Datatypes and Variables
With datatyping every variable is assigned to a datatype.
Why?
Well, IEC 1131-3 is designed to help you to find errors as early as possible in the programming phase.
As you all know, that is the fastest and cheapest way.
Now you know if the data is a string, a date, and integer or 16
bits of Boolean input.
There is no confusion about this anymore, and there is
no conflict between different people using the textual
representation (that means, the name of the variable)

## Slide 32: IEC 61131-3 : Common Elements
Data Types
such as:
BOOL BYTE
INTEGER : SINT, INT, DINT, LINT
USINT, UINT, UDINT, ULINT
REAL, LREAL
DATE
TIME_OF_DAY
DATE_AND_TIME
STRING
Notes: Examples of standard data types are Boolean, Byte Integer, Real, which you all probably know,
but also Date, Time_of_Day and String.
Datatyping avoids a lot of errors, like dividing an integer with a date.

## Slide 33: Variable Declaration
textual representation of usage type of variable
  scope: local (or global)
  explicit parameter passing via variables (inputs or outputs)
  memory allocation
declaration can include initial values
coupled to ‘Program Organization Unit’ (Function, Function Block or Program)

## Slide 34: Variable Declarations
Keyword Variable usage
VAR Internal to organization unit
VAR_INPUT Externally supplied, not modifiable within organization unit
VAR_OUTPUT Supplied by organization unit to external entities
VAR_IN_OUT Supplied by external entities. Can be modified within org. unit
VAR_EXTERNAL Supplied by configuration via VAR_GLOBAL .Can be modified within organization unit
VAR_GLOBAL Global variable declaration
VAR_ACCESS Access path declaration
RETAIN Retentive variables
CONSTANT Constant (variable cannot be modified)
AT Location assignment

## Slide 35: Variable Declarations : example
VAR
CONDITION_RED : BOOL;
IBOUNCE : WORD;
MYDUB : DWORD;
AWORD, BWORD, CWORD: INT;
OKAY : STRING[10] := ‘OK’;
END_VAR

## Slide 36: IEC 61131-3 : Common Elements
Data Types & Variables
in addition:
Your own datatypes
…
derived datatypes
Notes: In addition to these standard dataypes, you can create your
own
Once defined you can use them all over again
This can be very helpful within your own systems

## Slide 37: Derived Datatypes
Direct derivation from elementary types, e.g.: TYPE R : REAL ; END_TYPE
Enumerated data types, e.g.: TYPE ANALOG_SIGNAL_TYPE : (SINGLE_ENDED, DIFFERENTIAL) ; END_TYPE
Subrange data types, e.g.: TYPE ANALOG_DATA : INT (-4095..4095) ; END_TYPE
Array data types, e.g.: TYPE ANALOG_16_INPUT_DATA : ARRAY [1..16] OF ANALOG_DATA ; END_TYPE

## Slide 38: Your own datatype: derived datatype

## Slide 39: Your own datatype: derived datatype
TYPE ANALOG_DATA : INT (-4095..4095) ; END_TYPE

## Slide 40: Your own datatype: derived datatype
TYPE ANALOG_SIGNAL_TYPE : (SINGLE_ENDED, DIFFERENTIAL) ; END_TYPE

## Slide 41: Directly Represented Variables : %
Prefix Meaning Default data type
I Input location
Q Output location
M Memory location
X Single bit size BOOL
None Single bit size BOOL
B Byte (8 bits) size BYTE
W Word (16 bits) size WORD
D Double word (32 bits) size DWORD
L Long (quad) word (64 bits) size LWORD

## Slide 42: IEC 61131-3 : Common Elements
COMMON ELEMENTS
a.o.
Data Types & Variables
Configuration
Resources
Tasks
Notes: Back to the common elements
For this following part , we look at the defined Software Model.

## Slide 43: IEC 61131-3 Software Model
Configuration
Communication Function
Notes: At the highest level, the entire software required to solve a particular control problem is called a Configuration.

## Slide 44: IEC 61131-3 Software Model
Configuration
Communication Function
Resource
Resource
Notes: Within a configuration, one or more Resources can be defined.
A resource is like a CPU in your system.

## Slide 45: IEC 61131-3 Software Model
Task
Task
Task
Task
Resource
Resource
Configuration
Communication Function
Notes: A resource include one or more Tasks .
Tasks control the execution of different parts of programs…..

## Slide 46: IEC 61131-3 Software Model
Execution control path
Task
Program
Program
Task
Program
Task
Program
Task
Resource
Resource
Configuration
Communication Function
Notes: Programs can be written in any of the IEC languages

## Slide 47: IEC 61131-3 Software Model
Communication Function
Access path
Execution control path
FB
Task
Program
Program
FB
FB
Task
Program
Task
Program
FB
FB
Task
Resource
Resource
Configuration
Function Block
Notes: In the end programs call Functions or Function Blocks These are the basic building blocks with datastructure and algorithm

## Slide 48: IEC 61131-3 Software Model
Global and direct variables
Access path
Execution control path
Variable access path
FB
Task
Program
Program
FB
FB
Task
Program
Task
Program
FB
FB
Task
Resource
Resource
Configuration
Communication Function
Function Block
Variable
Notes: All these can exchange their information via the global or direct variables, even to the outside world via the communication function
Let us compare this to a conventional PLC……….

## Slide 49: IEC 61131-3 vs conventional PLC
Global and direct variables
Access path
Execution control path
Variable access path
FB
Task
Program
Program
FB
FB
Task
Program
Task
Program
FB
FB
Task
Resource
Resource
Configuration
Communication Function
Function Block
Variable
Notes: As shown here in red, a conventional PLC consists of one resource, running one task, controlling one program
As you can easily see, IEC 1131-3 can go well beyond conventional PLCs.
It can provide you with a state-of-the-art multitasking, real-time environment
This also makes IEC 1131 applicable to a much broader area as just PLCs. It can be used in a broad range of application area’s, without having to learn additional programming languages.

## Slide 50: Configuration Elements
Configuration
Resources
Tasks
Global Variables
Access Paths

## Slide 51: Configuration, Resources and Access Paths (-Declaration)
CONFIGURATION … END_CONFIGURATION
VAR_GLOBAL … END_VAR (within CONFIGURATION)
RESOURCE … ON … END_RESOURCE
VAR_GLOBAL … END_VAR (within RESOURCE)
PERIODIC TASK
NON-PERIODIC TASK

## Slide 52: IEC 61131-3 : Common Elements
COMMON ELEMENTS
a.o.
Data Types & Variables
Configuration, Resources, Tasks
Programming Organization Units
  Functions
  Function Blocks
  Programs
Notes: Within the common elements, the Functions, Function Blocks and Programs are called Program Organization Units.
They provide you re-usability from macro level to micro level.
Let us have a closer look at them,.
First the functions…...

## Slide 53: Functions …..
* Standard functions
ADD, SQRT, SIN, COS, GT, MIN, MAX, AND, OR, etc.
* Your own defined functions:
FUNCTION SIMPLE_FUN : REAL
VAR_INPUT
A, B : REAL;
C : REAL := 1.0;
END_VAR
SIMPLE_FUN := A*B/C;
END FUNCTION
Notes: We all know functions like Add, Square root, SINus, COSinus, Greater Than, etc.,
IEC has a enormous set of these defined.
You also can create your own functions like this simple_function
Once defined, you can use it over and over again…..
The same is valid for Function Blocks…..

## Slide 54: …. & Function Blocks
Standard Function Blocks
Notes: They are like the software equivalent of Integrated Circuits, ICs.
Like black boxes that represent a specialized control function
You have standard defined function blocks, like timers, counters and triggers….

## Slide 55: …. & Function Blocks
Standard Function Blocks
Additional supplied Function Blocks
Notes: ..and each supplier can add their own library of blocks, as long as they comply to the defined structure
A temperaure control loop, or PID, is an excellent example of such a Function Block.

## Slide 56: …. & Function Blocks
Standard Function Blocks
Additional supplied Function Blocks
Your own defined Function Blocks
Notes: And you can add your own library of Function Blocks

## Slide 57: …. & Function Blocks
Standard Function Blocks
Additional supplied Function Blocks
Your own defined Function Blocks
All FBs are highly re-usable in same program, different programs or project
Notes: No matter which Function Block, they are highly re-usable :
in the same program, different programs or even different projects.
You can use them with any of the IEC programming languages,
giving you a clear separation between different levels of programmers, or maintenance people.
Their re-usability increases your efficiency, and reduces the number of errors.

## Slide 58: Function Block example
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
1
EPS
EPS
0
XIN2
Q
Notes: Let’s look at an example.
Here shown is a function block in the programming language
Function Block Diagram
The FB has the name Hysterisis
It has three inputs, named XIN1, XIN2 and EPS, on the left
They are all of datatype REAL
It has one output (on the right hand side), called Q, of
type BOOL
Internally, the FB cotains body code…..

## Slide 59: Function Block example
FUNCTION_BLOCK HYSTERISIS
VAR_INPUT
XIN1, XIN2 : REAL;
EPS : REAL; (* Hysterisis band *)
END_VAR
VAR_OUTPUT
Q : BOOL := 0
END_VAR
IF Q THEN
IF XIN1 < (XIN2-EPS) THEN
Q := 0 (* XIN1 decreasing *)
END_IF;
ELSIF XIN1 > (XIN2 + EPS ) THEN
Q := 1; (* XIN1 increasing *)
END_IF;
END_FUNCTION_BLOCK
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
1
EPS
EPS
0
XIN2
Q
Notes: In this example, the body code is written in the language
Structured Text
It uses the inputs,does some calculation, and sets the outputs.
The first part deals with the data structure, the second half with
the algorithm
In this case it does not use additional data. But it could.
No matter which name was used for this local data
inside the body, there would be no conflict with its name:
one could use this name on different places, without conflict,
This examle of data encapsulation takes away a big source of errors.

## Slide 60: Programs : hierarchical design
Automation
application
Start : BOOL;
Emergency : BOOL;
Limit : INT;
PROGRAM
GLOBAL
Local
Type
FUNCTION
INPUT
Local
Type
FUNCTION_BLOCK
INPUT
OUTPUT
IN_OUT
EXTERNAL
Local
Type
Notes: With these Functions and Function Blocks , you can look at a program as a network of these basic building blocks.
In this way complex programs can be broken down into function blocks,
which again can be broken down into smaller function blocks.
This decomposition helps you increasing your efficiency .

## Slide 61: Programming Model

## Slide 62: IEC 61131-3 : Common Elements
COMMON ELEMENTS
a.o.
Data Types Variables
Program Organization Units
* Functions
* Function Blocks
* Programs
Configuration, Resources, Tasks
Sequential Function Chart
* Steps
* Transitions
* Actions Blocks
Notes: Back to the overview of the common elements.
As you can see there is one topic left. Let’s deal with it now

## Slide 63: Sequential Function Chart, SFC
Powerful graphical technique for describing the sequential behaviour of a control program
Used to partition a control problem
Shows overview, also suitable for rapid diagnostics
Step 1 N FILL
Step 3
Step 2 S Empty
Transition 1
Transition 2
Notes: When two or more transitions are associated with leaving a step, one can select alternative steps in a sequence using a divergence construct
One can use this also to provide alternative sequences.
As ultimate, the standard also support parallel sequences, such as commonly required in batch applications.
For instance, one sequence is is used for the primary process, and the second for monitoring the overall operating constraints.
And this all within the same overview and structure.

## Slide 64: Sequential Function Chart, SFC
Powerful graphical technique for describing the sequential behaviour of a control program
Used to partition a control problem
Shows overview, also suitable for rapid diagnostics
The basic elements are STEPS with ACTION BLOCKS and TRANSITIONS
Support for alternative and parallel sequences
Step 1 N FILL
Step 3
Step 2 S Empty
Transition 1
Transition 2
Notes: When two or more transitions are associated with leaving a step, one can select alternative steps in a sequence using a divergence construct
One can use this also to provide alternative sequences.
As ultimate, the standard also support parallel sequences, such as commonly required in batch applications.
For instance, one sequence is is used for the primary process, and the second for monitoring the overall operating constraints.
And this all within the same overview and structure.

## Slide 65: The IEC 61131-3 Standard
Common Elements
Programming Languages
Top Down
Bottom Up
Notes: There is more,
and it is directly related to the development systems, which by the way are called PSE’s in IEC, or Program Support Environments.
If we look to the simple picture of the IEC 1131-3 standard, the standard allows two ways to develop your program: bottom up and top down
Whichever you chose, the environment will help you through the whole process
After all, software is here to help us……..

## Slide 66: IEC Programming Environments
Many of them offer:
graphical programming screens
support for multiple windows
mouse operation
pull-down menus
built-in hypertext help function
software verification during design
Notes: and they do..
Many IEC programming systems offer you all you expect from modern environments.
Some of the features are listed here
Compare that to the cryptic character based systems, and you have an additional reason
We mentioned several advantages of this standard
Let us summarize them…….

## Slide 67: Common Elements
Sequential Function Chart
See separate presentation