## Slide 1: Introduction to IEC1131-3 Ladder Diagram

## Slide 2: Origins of Ladder Diagram
CPU
The Ladder Diagram (LD) programming language originated from the graphical representation used to design an electrical control system
  Control decisions were made using relays
After a while Relays were replaced by logic circuits
  Logic gates used to make control decisions
Finally CPUs were added to take over the function of the logic circuits
  I/O Devices wired to buffer transistors
  Control decisions accomplished through programming
Relay Logic representation (or LD) was developed to make program creation and maintenance easier
  Computer based graphical representation of wiring diagrams that was easy to understand
  Reduced training and support cost
OR
AND

## Slide 3: What is a Rung?
A rung of ladder diagram code can contain both input and output instructions
  Input instructions perform a comparison or test and set the rung state based on the outcome
    Normally left justified on the rung
  Output instructions examine the rung state and execute some operation or function
    In some cases output instructions can set the rung state
    Normally right justified on the rung
Input Instruction
Output Instruction

## Slide 4: Series Vs Parallel Operations
Ladder Diagram input instructions perform logical AND and OR operations in and easy to understand format
  If all Input Instructions in series must all be true for outputs to execute (AND)
  If any input instruction in parallel is true, the outputs will execute (OR)
Paralleling outputs allows multiple operations to occur based on the same input criteria
OR
AND
A
B
C
D
IF ((A OR B) AND (NOT C) AND D) THEN E=1; F=1 END_IF
E
F
Branches

## Slide 5: Ladder Logic Execution
Rungs of Ladder diagram are solved from Left to right and top to bottom
Branches within rungs are solved top left to bottom right
P
S
R
A
B
D
E
F
G
H
I
J
K
Left Power Rail
Branch
Right Power Rail
Ladder Rung

## Slide 6: Non Retentive Coils
The referenced bit is reset when processor power is cycled
  Coil -( )-
    Sets a bit when the rung is true(1) and resets the bit when the rung is false (0)
    PLC5 calls this an OTE Output Enable
  Negative coil -( / )-
    Sets a bit when the rung is false(0) and resets the bit when the rung is True(1)
    Not commonly supported because of potential for confusion
  Set (Latch) coil -(S)-
    Sets a bit (1) when the rung is true and does nothing when the rung is false
  Reset (Unlatch) Coil -(R)-
    Resets a bit (0) when the rung is true and does nothing when the rung is false

## Slide 7: Contacts
Normally Open Contact -| |-
  Enables the rung to the right of the instruction if the rung to the left is enabled and underlining bit is set (1)
Normally Closed Contact -|/|-
  Enables the rung to the right of the instruction if the rung to the left is enabled and underlining bit is reset (0)
Positive transition contact -|P|-
  Enables the right side of the rung for one scan when the rung on left side of the instruction is true
  Allen Bradley PLC5 uses -[ONS]-
Negative transition contact -|N|-
  Enables the right side of the rung for one scan when the rung on left side of the instruction is false

## Slide 8: Retentive Vs Non-retentive Operation
Definitions
  Retentive values or instructions maintain their last state during a power cycle
  Non-retentive values or instructions are reset to some default state (usually 0) after a power cycle
IEC1131 permits values to be defined as retentive
  A contradiction to this is ladder diagram where 3 instructions are classified as retentive
  In most PLCs only timer and coil instructions operate as non-retentive

## Slide 9: Retentive Coils
The referenced bit is unchanged when processor power is cycled
  Retentive coil -(M)-
    Sets a bit when the rung is true(1) and resets the bit when the rung is false (0)
  Set Retentive (Latch) coil -(SM)-
    Sets a bit (1) when the rung is true and does nothing when the rung is false
    PLC5 uses OTL Output Latch
  Reset Retentive (Unlatch) Coil -(RM)-
    Resets a bit (0) when the rung is true and does nothing when the rung is false
    PLC5 uses OUT Output Unlatch

## Slide 10: Transition Sensing Coils
Positive transition-sensing coil -(P)-
  Sets the bit bit (1) when rung to the left of the instruction transitions from off(0) to on(1)
  The bit is left in this state
  PLC5 use OSR (One Shot Rising)
Negative transition-sensing coil -(N)-
  Resets the bit (0) when rung to the left of the instruction transitions from on(1) to off(0)
  The bit is left in this state
  PLC5 uses OSF (One Shot Falling)

## Slide 12: IEC Comparison Instructions in Ladder
If the rung input (EN) is enabled, the instruction performs the operation and sets the rung output (ENO) based on the comparison
  Example: when EN is true, EQ (=) function compares In1 and to In2 and sets ENO
Comprehensive instruction set
  EQ(=), GT (>), GE (>=), LT (<), LE (<=), NE (<>)
EQ
EN
100.000
ENO
78.251
Tank_max
Tank1_Level
IN1
IN2

## Slide 13: Timers in Ladder Diagram
There three timer instructions in IEC1131
  TP - Pulse timer
  TON - Timer On Delay
  TOF - Timer Off Delay
Time values
  Time base is 1msec (1/1000 of a sec)
  Values entered using duration literal format
Two possible visualizations Depending on use of EN/ENO
  1st method requires extra programming if timer done status needs to be referenced on other rungs
  2nd method sets a bit with Q which can be referenced by other logic, ENO=EN
TON
IN
T#200ms
Pump_Tmr
PT
ET
178
Q
TON
T#200ms
Pump_Tmr
PT
ET
178
Q
IN
ENO
Pump_Tmr_DN

## Slide 14: Timer Operation
IN
Q
ET
PT
|
0
Pulse (TP) Timing
IN
Q
ET
PT
|
0
On-Delay (TON) Timing
IN
Q
ET
PT
|
0
Off-Delay (TOF) Timing
IN = Rung input condition
Q = Comparison output results
  Varies with timer types
PT = Preset Time
ET = Elapse Time

## Slide 15: Counters in Ladder Diagram
There three counter instructions in IEC1131
  CTU - Count Up Counter
  CTD - Count Down Counter
  CTUD - Count Up/Down Counter
All three count rung transitions
Two possible visualizations Depending on use of EN/ENO
  1st method requires extra programming if timer done status needs to be referenced on other rungs
  2nd method sets a bit with Q which can be referenced by other logic, ENO=EN
CTU
200
Load_Cnt
PV
CV
178
Q
IN
ENO
Load_Cnt_DN
R
CTU
200
Load_Cnt
PV
CV
178
Q
IN
R

## Slide 16: Counter Operation
Parameters
  CU/CD = Count up/Down
  Q/QU/QD = Comparison Output
  R = Reset to Zero
  LD = Load CV with PV
  PV = Preset Value
  CV = Count Value
...
...
CV
PV
|
0
CU
QU
CD
QD
LD
R
Count Up/Down (CTUD) Counter
...
IN
Q
CV
PV
|
0
LD
...
Count Down (CTD) Counter
...
IN
Q
CV
PV
|
0
R
Count Up (CTU) Counter
...

## Slide 17: Execution Control Elements
CAL
RET
RET
CAL
Jump / Label Instructions
  Jump to a label skips a block of code without it being scanned
  LBL - Named target for a jump operation
  JMP - Performs a jump when the rung conditions are true
CALL / RETURN Instructions
  Used to encapsulate logic and call it as a subroutine
  Causes execution to change between functions or subroutines
  CAL - Passes control to another named function
    PLC5 uses JSR
  RET - Exits a function and returns control back to the calling routine
| Skip_Calc |
|-| |-------------(JMP)--|
| ... |
| Skip_Calc |
|---[LBL]---...

## Slide 18: Different Instruction Presentations
The look and feel of IEC 1131-3 is somewhat different from the 1Million+ PLC’s that Allen Bradley has running in factories throughout the world
IEC places the input parameters on the outside of the instruction block vs the PLC5 where they are presented inside of the block
TON
Timer
Preset
Pump_Tmr
200.000
Accum
178.251
(EN)
(DN)
ADD
Source A
Source B
Tank1_In
Offsetr
Destination
Tank_Level
178.251
78.251
100.000
+
EN
100.000
178.251
ENO
78.251
Offsetr
Tank1_In
Tank_Level
TON
T#200ms
Pump_Tmr
PT
ET
178
Q
IN
ENO
Pump_Tmr_DN

## Slide 19: Extending the IEC1131-3 Instruction Set
IEC1131-3 Provides a very basic set of instructions to do simple operations (81 Ladder Diagram Instructions)
  Data Type Conversion - Trunc, Int_to_Sint, Dint_to_Real, Bcd_To_Int …
  Boolean Operations - Bit Test, Bit Set, One Shot, Semaphores …
  Timers / Counters - Ton, Tp, Ctu, Ctd, Ctud
  Simple Math - Add, Sub, Mul, Div, Mod, Move, Expt
  Misc. Math - Abs, Sqrt, Ln, Log, Exp, Sin, Cos, Tan, Asin, Acos, Atan
  Bit Shift - Shl, Shr, Ror, Rol
  Logic - And, Or, Xor, Not
  Selection - Sel, Max, Min, Limit, Mux
  Compare - GT, GE, EQ, LE, LT, NE
  String - Len, Left, Right, Mid, Concat, Insert, Delete, Replace, Find
  Control - JMP, LBL, JSR, RET
All complex operations are left to the user or vendor to define
  File Operations, PID, Diagnostic, For/Nxt Loop, Search, Sort are not in IEC1131-3
  Extensions to the instruction set are permitted so that vendors can add instructions that their customers need
  All vendors have defined their own set of extensions
  Rockwell Automation controllers have significantly more capability with over 130 Ladder Instructions

## Slide 20: Extensions to IEC provide code optimization and ease of use
=
Rockwell Automation FIFO Load Instruction
IEC1131-3 Load FIFO Logic
1 Rung of Logic
1 Instruction
Minutes to code and debug
11 Rungs of Logic
17 Instructions
Hours to code and debug

## Slide 21: Rockwell Automation Instruction Extension to IEC1131-3
FIFO & LIFO - FFL, FFU, LFL, LFU
File math and search - FAL, FSC
Table operations - SRT, STD, AVE
Sequencers - SQI, SQL, SQO, SDS
Diagnostics - DDT, DFA, FBC
Compare - CMP, MEQ
Compute - CPT, NEG
Data moves - MVM, COP, BTD
Program Control - AFI, NOP, MCR, TND
Interrupt Services - UID, UIE
Retentive Timer - RTO
Ladder Loop Instruction - FOR, NXT
Process - PID
Motion - 30+ instructions to perform closed loop servo control